## Slide 1
Electromagnetic Induction
& Alternating Current
Class 12 Physics · Units 6 & 7
Notes: Welcome slide. Introduce the two closely related units: Electromagnetic Induction (Faraday's Laws, Lenz's Law, inductance) and Alternating Current (AC generators, RLC circuits, resonance, transformers). These topics form the backbone of modern electrical engineering and power systems.

## Slide 2
Topics at a Glance
⚡ EM Induction
Faraday's Laws, Lenz's Law, Motional EMF, Eddy Currents
🔁 Inductance
Self-Inductance, Mutual Inductance, Energy in Inductor
〜 AC Fundamentals
Generation, Peak & RMS Values, Phase Relationships
🔌 AC Circuits
Phasors, Impedance, Power Factor, LCR Resonance
🔋 Transformers
Step-Up / Step-Down, Efficiency, Power Transmission
Notes: This slide gives students an overview of all the topics covered in this presentation. Use it to set expectations and show how EM induction leads naturally into AC current concepts.

## Slide 3
Faraday's Laws of Electromagnetic Induction
First Law: An EMF is induced in a conductor when the magnetic flux through it changes.
Second Law: The magnitude of induced EMF equals the rate of change of magnetic flux linkage.
ε = −N (dΦ/dt)
Induced EMF (Faraday's Law)
Φ = B · A · cos θ
Magnetic Flux
ε = −dΦ_linkage/dt
Flux Linkage (NΦ)
Key Terms: Magnetic Flux (Φ) — Weber (Wb) | Flux Linkage = NΦ | EMF unit: Volt (V) | N = Number of turns
💡 Flux Rule Summary • Flux increases → Induced current opposes increase
• Flux decreases → Induced current supports the original field
• Flux constant → No induced EMF (ε = 0)
Notes: Faraday's First Law establishes that any change in magnetic flux induces EMF. The Second Law gives the quantitative relationship. The negative sign (from Lenz's Law) indicates the direction of induced EMF opposes the change. Emphasise that it is the RATE of change, not the magnitude of flux, that matters.

## Slide 4
Lenz's Law & Conservation of Energy
"The direction of the induced current is such that it opposes the cause producing it."
🔑
Statement: Induced EMF always opposes the change in magnetic flux (consequence of energy conservation).
⚖️
Energy Link: Work done against opposing force = Electrical energy generated; no energy is created from nothing.
🔄
Right-Hand Rule: Curl fingers in direction of induced current; thumb points in direction of induced B-field.
📐
Sign in formula: The minus sign in ε = −N(dΦ/dt) mathematically represents Lenz's Law.
Notes: Lenz's Law is a statement of energy conservation. If the induced current aided the cause, it would create more flux, induce more current — a perpetual motion machine. Encourage students to relate the minus sign in Faraday's equation directly to this law.

## Slide 5
Motional EMF & Eddy Currents
Motional EMF
When a conductor of length L moves with velocity v perpendicular to field B:
ε = BLv
B ⊥ v ⊥ L
ε = BLv sin θ
General case (angle θ)
Eddy Currents
• Induced in bulk conductors in changing B-fields
• Cause energy loss as heat (I²R)
• Minimised by using laminated cores
• Applications: magnetic braking, induction heating, metal detectors
Applications of Motional EMF:
• Electric generators convert mechanical energy → electrical energy using motional EMF
• Search coils (flux meters) measure magnetic fields
• Railgun technology uses the F = BIL force in reverse of motional EMF principle
Notes: Motional EMF is key to understanding how generators work — mechanical motion is converted to electrical energy. Eddy currents are important for understanding core losses in transformers and motors, and students should know both their harmful effects and useful applications.

## Slide 6
Self-Inductance & Mutual Inductance
Self-Inductance (L)
A coil opposes any change in current through it by inducing a back-EMF.
L = NΦ / I
Inductance (Henry, H)
ε = −L (dI/dt)
Back-EMF
L = μ₀μᵣN²A / l
For solenoid
Mutual Inductance (M)
EMF induced in one coil due to changing current in a nearby coil.
M = N₂Φ₂₁ / I₁
Mutual Inductance
ε₂ = −M (dI₁/dt)
Induced EMF in coil 2
M = k√(L₁L₂)
Coefficient of coupling
Energy stored in an inductor: U = ½LI² (analogous to ½mv² in mechanics)
Unit of Inductance: Henry (H) = Vs/A = Ω·s | k = coupling coefficient (0 ≤ k ≤ 1)
Notes: Self-inductance is the inertia of electrical circuits — a coil resists changes in current just as mass resists changes in velocity. Mutual inductance is the operating principle of transformers. The coupling coefficient k = 1 for an ideal transformer.

## Slide 7
Generation of Alternating Current
An AC generator (alternator) converts mechanical energy into electrical energy using electromagnetic induction.
🔄
Armature Coil: Rectangular coil (ABCD) that rotates in the magnetic field.
🧲
Field Magnets: Provide a uniform magnetic field (permanent or electromagnets).
💍
Slip Rings: Allow continuous rotation; connected to the rotating coil.
🖊️
Brushes: Stationary carbon contacts that collect current from slip rings.
⚡
Output: Sinusoidal alternating EMF: ε = ε₀ sin(ωt)
Notes: The AC generator is a direct application of Faraday's Law. As the coil rotates at angular velocity ω, the flux changes sinusoidally, producing a sinusoidal EMF. Slip rings (vs. commutator in DC) allow bidirectional current flow. Emphasise why AC is preferred over DC for power transmission.

## Slide 8
AC Quantities: Peak, RMS & Average Values
Key Expressions
ε = ε₀ sin(ωt)
Instantaneous EMF
I = I₀ sin(ωt − φ)
Instantaneous Current
Iᵣₘₛ = I₀ / √2 ≈ 0.707 I₀
RMS Current
Vᵣₘₛ = V₀ / √2 ≈ 0.707 V₀
RMS Voltage
I_avg = 2I₀/π ≈ 0.637 I₀
Average (half-cycle)
ω = 2πf = 2π/T
Angular Frequency
Comparison Table
Quantity | Symbol | Relation to Peak
RMS Voltage | Vᵣₘₛ | V₀/√2
RMS Current | Iᵣₘₛ | I₀/√2
Avg Voltage | V_avg | 2V₀/π
Form Factor | F | Iᵣₘₛ/I_avg ≈ 1.11
Peak Factor | P | I₀/Iᵣₘₛ = √2 ≈ 1.41
Notes: RMS values are the DC equivalent values that produce the same heating effect. The household supply of 230V is an RMS value — peak voltage is about 325V. Form factor and peak factor are important for understanding waveform characteristics and for designing rectifier circuits.

## Slide 9
Phasors & Phase Relationships in AC Circuits
A phasor is a rotating vector that represents a sinusoidal quantity. Its projection on the y-axis gives the instantaneous value.
Pure Resistor (R)
Phase: V & I in phase (φ = 0°)
Voltage:
V = V₀ sin ωt
Current:
I = I₀ sin ωt
Impedance:
Z = R
Pure Inductor (L)
Phase: I lags V by 90° (φ = +90°)
Voltage:
V = V₀ sin ωt
Current:
I = I₀ sin(ωt−90°)
Impedance:
X_L = ωL
Pure Capacitor (C)
Phase: I leads V by 90° (φ = −90°)
Voltage:
V = V₀ sin ωt
Current:
I = I₀ sin(ωt+90°)
Impedance:
X_C = 1/(ωC)
Notes: Phasors simplify AC circuit analysis by converting differential equations into algebraic ones. The three cases (R, L, C) must be memorised. A useful mnemonic: CIVIL — In a Capacitor, I leads V; V leads I in an inductor (L). Emphasise that phase difference is between V and I, not between different voltages.

## Slide 10
LCR Series Circuit & Impedance
In a series LCR circuit, the same current I flows through all elements but voltages are out of phase.
X_L = ωL
Inductive Reactance (Ω)
X_C = 1/(ωC)
Capacitive Reactance (Ω)
Z = √(R² + (X_L−X_C)²)
Impedance Z (Ω)
tan φ = (X_L−X_C)/R
Phase Angle φ
I = V/Z
Current (Ohm's Law for AC)
P = Vᵣₘₛ Iᵣₘₛ cos φ
True Power (W)
Impedance Triangle
• Hypotenuse = Z | Horizontal = R | Vertical = (X_L − X_C)
• cos φ = R/Z (Power Factor) | sin φ = (X_L−X_C)/Z
• When X_L > X_C: circuit is inductive (I lags V) | When X_C > X_L: capacitive (I leads V)
Notes: The LCR series circuit is the most important circuit in this chapter. Draw the phasor diagram alongside the impedance triangle. Students often confuse the two — the phasor diagram is for voltages; the impedance triangle is for resistance and reactances. The power factor cos φ = R/Z is crucial for practical AC circuits.

## Slide 11
Resonance in LCR Circuit
Resonance occurs when X_L = X_C, making impedance purely resistive (Z = R, minimum) and current maximum.
ω₀ = 1/√(LC)
Resonant Angular Frequency
f₀ = 1/(2π√LC)
Resonant Frequency (Hz)
Q = ω₀L/R = 1/(ω₀CR)
Quality Factor (Q-factor)
Bandwidth = R/L = ω₀/Q
Bandwidth (Δω)
I_max = V/R (at resonance)
Maximum Current
Properties at Resonance:
• Z is minimum (= R); Current I is maximum
• Power factor cos φ = 1 (purely resistive behaviour)
• Voltage across L and C may be much larger than supply voltage (voltage magnification = Q)
• Higher Q → sharper resonance peak → better frequency selectivity (used in radio tuning)
Notes: Resonance is the most fascinating phenomenon in AC circuits. The Q-factor tells us how sharp the resonance is — a radio receiver needs high Q to select one station from many. At resonance, voltages across L and C can exceed supply voltage by a factor of Q, which can be large (in practice, 100 or more).

## Slide 12
Power in AC Circuits
True (Active) Power (P)
Formula: P = Vᵣₘₛ Iᵣₘₛ cos φ | Unit: Watt (W)
Actual power consumed; does useful work. Maximum when cos φ = 1.
Reactive Power (Q)
Formula: Q = Vᵣₘₛ Iᵣₘₛ sin φ | Unit: VAR
Energy oscillating between source and L/C; does no net work.
Apparent Power (S)
Formula: S = Vᵣₘₛ × Iᵣₘₛ | Unit: Volt-Ampere (VA)
Total power supplied by source; S² = P² + Q².
Power Factor cos φ = P/S = R/Z | Ideal circuits: cos φ = 1 | Pure L or C: cos φ = 0 (wattless current)
Notes: Power in AC circuits is subtle because voltage and current are rarely in phase. True power alone does useful work. Wattless (reactive) current in inductors and capacitors increases the apparent load on the supply without doing useful work. Power companies penalise low power factors by charging for apparent power.

## Slide 13
Transformers
A transformer transfers electrical energy between two circuits through mutual induction, changing voltage and current levels.
Vₛ/Vₚ = Nₛ/Nₚ = Iₚ/Iₛ
Transformer Ratio (ideal)
η = (Pₒᵤₜ/Pᵢₙ) × 100%
Efficiency η
Step-Up Transformer
Nₛ > Nₚ → Vₛ > Vₚ → Iₛ < Iₚ
Used in power transmission to increase voltage and reduce current (less I²R losses).
Step-Down Transformer
Nₛ < Nₚ → Vₛ < Vₚ → Iₛ > Iₚ
Used at consumer end to reduce high transmission voltage to safe usable levels (230 V).
Energy Losses in Transformers:
• Copper loss (I²R heating in windings) • Iron/Core loss (hysteresis + eddy currents — minimised by laminated silicon steel core)
• Flux leakage (not all flux links both coils) • Dielectric losses in insulation
Notes: Transformers are why AC is used for power transmission globally. An ideal transformer conserves power: VₚIₚ = VₛIₛ. Real transformers are 95–99% efficient. The turn ratio is the key parameter — students should be comfortable calculating voltages, currents, and turns for both step-up and step-down configurations.

## Slide 14
Real-World Applications
⚡
Power Grids
Step-up transformers (400 kV) minimise transmission losses; step-down brings 230V to homes.
📻
Radio Tuning
Variable capacitor tunes the resonant frequency of an LCR circuit to select a station.
🏭
Induction Heating
Eddy currents in a metal workpiece generate heat for welding, melting, and hardening steel.
🚂
Maglev / Braking
Eddy current braking in high-speed trains provides smooth, contact-free deceleration.
💡
Electric Motors
AC induction motors use rotating magnetic fields produced by 3-phase alternating current.
🔍
Metal Detectors
A transmit coil induces eddy currents in metal objects; secondary coil detects the response.
Notes: Connecting theory to real-world applications motivates students. Each application can be a discussion starter. Ask students: why is 50Hz chosen as the supply frequency? (It is a trade-off between transformer size and lighting flicker.) Why high voltage for transmission? (P_loss = I²R; high V → low I → low loss.)

## Slide 15
Key Takeaways
1. Faraday's Laws quantify induced EMF: ε = −N dΦ/dt; Lenz's Law gives direction (conservation of energy).
2. Motional EMF: ε = BLv; Eddy currents cause losses but enable braking & heating.
3. Self/Mutual Inductance: L = NΦ/I; M = k√(L₁L₂); Energy = ½LI².
4. AC quantities: Vᵣₘₛ = V₀/√2; phasors simplify R, L, C circuit analysis.
5. LCR series: Z = √(R²+(X_L−X_C)²); resonance at ω₀ = 1/√LC (max I, min Z).
6. Power: P = Vᵣₘₛ Iᵣₘₛ cos φ; Power factor (cos φ) crucial for efficiency.
7. Transformers: Vₛ/Vₚ = Nₛ/Nₚ; enable long-distance AC power transmission.
Notes: Summarise the entire chapter in these 7 points. Encourage students to make their own formula sheet. Suggest practice problems: (1) Calculate induced EMF for rotating coil; (2) Find resonant frequency; (3) Calculate transformer turns ratio; (4) Calculate power factor and true power in LCR circuit. End with: 'These principles power every electronic device you own.'